## Slide 1: Autonomous Sailboat
Thomas Gwynne-Timothy
&
JULIA SARTY

## Slide 2: Overview
Background
Goals & Responsibilities
Hardware Architecture
Software Architecture
I/O Layer
Task Layer
Control Layer
Future Work
Summary

## Slide 3: Background
“The Microtransat Challenge is a transatlantic race for autonomous boats. The race aims to stimulate the development of autonomous boats through friendly competition.”

## Slide 4: Goals & Responsibilities
Project Goals
Complete the Microtransat challenge
Improve boat performance and reliability
Improve data logging and system status feedback
UW-Stream Team Responsibilities
Transfer control from PIC to ARM
Restructure source code for improved maintainability and reliability
Develop communication system for data logging and remote control

## Slide 5: Hardware Architecture
UART
  GPS
  Wind
  XBee
  Xeos
I2C
  Compass
  EEPROM
Motors
  ADC
  PWM

## Slide 6: Software Architecture

## Slide 7: I/O Layer – UART & I2C
Allows communication to/from peripherals
UART (Universal Asynchronous Receiver Transmitter)
  4 channels
  Interrupt-driven (non-blocking) interface
  FIFO buffers for each channel
I2C (Inter-Integrated Circuit)
  2 slave devices
  Blocking interface

## Slide 8: I/O Layer – ADC & PWM
Allows control over motors
ADC (Analog-to-Digital Converter)
  2 channels for winch potentiometer and rudder potentiometer
  12-bit resolution
  Blocking interface
PWM (Pulse-Width Modulation)
  2 channels for winch motor and rudder motor
  500 Hz frequency
  250 duty cycle settings

## Slide 9: Task Layer – Communication
3-layer communication stack
  Application layer
  Data-link layer
  Physical layer
NMEA 0183
  Links application layer to physical layer
  Adds header, footer, and checksum

## Slide 10: Task Layer – Communication
Custom NMEA 0183 format
$DALSAIL,<type>,<arg1>,…,<argn>*checksum\r\n
Message types include:
  Data logging
  Remote control
  Way point mission loading
  Message acknowledgment

## Slide 11: Sailboat Dashboard

## Slide 12: Task Layer – Motors
Proportional control with closed-loop feedback

## Slide 13: Control Layer – Navigation
Update sailboat course
  Use way point, GPS location, boat heading, and wind direction to set a course
  Avoid dead zone with tacking
  Avoid running with jibing
  Set sail angle with pre-set positions
Maintain sailboat course
  Adjust rudder to maintain course

## Slide 14: Control Layer – Task Management
Tasks initiated with a control timer
Time stamps used to control timing between tasks
Watchdog timer used to prevent deadlock
static void ControlTimerTick(void)
{
  // Update the system clock
  t_ms += dt_ms;
  // Iterate through tasks
  for (int i = 0; i < CTRL_NUM_TASKS; i++) {
    // Check if it is time to run the task
    if (t_ms >= task_stamps_ms[i]) {
      // Run the task
      (*tasks[i])();
      // Update the time stamp
      task_stamps_ms[i] += task_periods_ms[i];
    }
  }
  // Reset the watchdog
  PetWatchDoge();
}

## Slide 15: Future Work
Ocean testing
Navigation tuning
Sea-state detection
Launch!

## Slide 16: Summary
Transfer control from PIC to ARM
Restructure source code for improved maintainability and reliability
Develop communication system for data logging and remote control